## Slide 1
PROJECT REVIEW 2 PRESENTATION
Range-Aware Edge AI
Quantization Compiler
SSA-Based Static Analysis for Safe FP32 → INT8 Optimization
SRC
AST
SSA
RANGE
INT8
Course: BCSE307L — Compiler Design
Yash Pradhan (24BCE0702) • Anjini Pandey (24BCE0714) • Ishita Srivastava (24BDS0234)
Faculty Guide: Prof. Kanagaraj R
Notes: Good morning. I'll be presenting my Compiler Design project review: a Range-Aware Edge AI Quantization Compiler. This is a compiler-optimization project that uses SSA and static range analysis to decide, at compile time, when FP32 values can be safely represented as INT8.

## Slide 2
INTRODUCTION
A Compiler Pass for Safety-Aware Precision Reduction
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
2
The Range-Aware Edge AI Quantization Compiler is a teaching-scale compiler that examines whether supported numerical values can be represented as INT8 before rewriting them. It makes the analysis and decision visible across compiler stages rather than relying on blind datatype replacement.
Why reduced precision?
Edge devices can face memory, compute and energy constraints. FP32 uses 4 bytes per value; INT8 uses 1 byte, reducing storage per quantized value.
Why not cast blindly?
A value may exceed [−128,127], be fractional, or change downstream results. Range alone is not enough to justify conversion.
What this project does
SSA exposes individual definitions; static range and integrality analysis feed conservative safety rules. Unproven values remain unchanged.
SSA IR
Versioned values
→
Range + integrality
Infer bounds and integer property
→
Safety gate
Check bounds and supported operation
→
Selective rewrite
Only proven-safe values
Purpose: demonstrate an explainable, source-traceable compiler optimization over a small C-like language — not a full ML framework.

## Slide 3
PROBLEM
Why Precision Matters at the Edge
Edge Device Constraints
M
Memory
Limited RAM/flash for weights and intermediate values.
C
Compute
Restricted CPU/accelerator throughput vs. server GPUs.
E
Energy
Battery-powered operation favors low-power arithmetic.
D
Data Movement
Off-chip memory access dominates cost in many workloads.
FP32
32-bit floating point → higher storage & compute cost per value
INT8
8-bit integer → lower storage footprint
But converting FP32 → INT8 blindly is unsafe — the compiler must first prove it is safe for each value.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
3
Notes: Edge devices are constrained in memory, compute, energy and data movement. FP32 uses 4 bytes per value while INT8 uses 1 byte, so precision reduction is attractive — but only if it can be done safely, which motivates the rest of the project. We do not claim automatic runtime or energy gains without measurement.

## Slide 4
PROBLEM STATEMENT
The Central Question
“Can a compiler statically determine which numerical computations can be safely represented using INT8, and transform only those computations for which safety can be proven?”
FP32 Value
Can the compiler prove:
Bounded range within [−128, 127]?
Value guaranteed integral?
No possible overflow?
Operation supported for quantization?
YES → Quantize to INT8
NO → Preserve FP32
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
4
Notes: This is the precise research question: not 'should we quantize', but 'can the compiler prove it is safe'. If the four proof obligations hold, we quantize; otherwise we conservatively keep FP32. This slide is the one I'd point to in a viva.

## Slide 5
MOTIVATION
Why Compiler-Based Analysis?
Manual Conversion
Error-prone, difficult to scale across programs
Dynamic / Runtime Checking
Correct, but adds overhead on every execution
Static Compiler Analysis
Decision made once, before execution — our approach
The compiler inspects intermediate representation and reasons about value ranges before performing the optimization — the safety decision is explainable and made once, at compile time.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
5
Notes: Manual precision conversion doesn't scale and is error-prone. Dynamic checking works but adds runtime cost on every execution. Static compiler analysis lets us make the safety decision once, at compile time, by reasoning directly over the IR.

## Slide 6
OBJECTIVES
Project Objectives
1
Build a small numerical C-like compiler front end.
Lexer, parser and AST for a deliberately compact language.
2
Generate Three Address Code and construct CFG.
Lower AST to TAC and form basic blocks.
3
Convert the IR into SSA form.
Enable precise, flow-sensitive analysis.
4
Perform static range and integrality analysis.
Interval reasoning over SSA values, including loops.
5
Develop conservative INT8 safety checks.
Reject whenever safety cannot be proven.
6
Transform proven-safe computations to INT8 IR.
Quantize only what is provably safe.
7
Preserve source-level traceability throughout.
Line/column tracked from lexer to diagnostics.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
6
Notes: Seven concrete objectives: from the front end through SSA, range and integrality analysis, conservative safety checks, the quantization transform itself, and source-level traceability so diagnostics can point back to the original code.

## Slide 7
LITERATURE SURVEY
Research Landscape
Edge AI / Efficient Inference
Resource-constrained deployment of ML workloads on devices.
Quantization / Reduced Precision
Representing values/weights with fewer bits (e.g. INT8).
Compiler-Based Optimization
Using compiler passes/IR to drive performance transformations.
Static Analysis / SSA
Flow-sensitive, provable reasoning over program values.
This Project — Intersection of all four areas
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
7
Notes: The literature spans four areas: Edge AI, quantization, compiler optimization, and static analysis / SSA. This project sits deliberately at the intersection — it is a compiler that uses SSA-based static analysis to make a quantization decision.

## Slide 8
LITERATURE SURVEY
Key Related Work
Work | Main Idea | Relevance | Difference from Our Project
Zhou et al. [1] Proc. IEEE 2019 | Survey of edge intelligence and on-device AI systems | Frames memory, compute and energy constraints at the edge | Motivates the application; no compiler or per-value safety proof
Chen & Ran [2] Proc. IEEE 2019 | Review of deep learning with edge computing | Covers deployment, compression and edge/cloud trade-offs | Model/system-level review rather than an IR optimization
Jacob et al. [3] CVPR 2018 | Integer-only inference with quantization-aware training | Shows the practical relevance of INT8 inference | Neural-network quantization; we analyze a small program IR
Krishnamoorthi [4] arXiv 2018 | Practical guide to post-training and QAT quantization | Explains scaling, calibration and quantization choices | Model-level practice, not per-value static proof
Cousot & Cousot [5] ISOP 1976 | Static determination of dynamic program properties | Foundational interval/range abstraction | General static analysis; applied here to INT8 eligibility
Cousot & Cousot [6] POPL 1977 | Abstract interpretation and fixed-point analysis | Grounds conservative data-flow reasoning | General framework; project uses a narrow interval domain
Bourdoncle [7] LNCS 735, 1993 | Widening/narrowing for chaotic iteration | Informs bounded loop-analysis convergence | General convergence method at teaching-scale scope
Blanchet et al. [8] PLDI 2003 | Astrée static analysis for safety-critical software | Demonstrates range analysis for run-time error proofs | Industrial-scale analyzer; ours targets a small language
Reference numbering follows the accompanying Review 2 Report: [1]–[8]. Papers [9]–[12] continue on the next slide.
Notes: Eight sources across four themes: INT8 quantization (Jacob, Krishnamoorthi, Han), the Edge AI motivation (Sze), compiler-driven optimization (TVM), and the static-analysis foundations we build on directly — SSA construction (Cytron et al.), abstract interpretation (Cousot & Cousot), and SSA-based range analysis on LLVM IR (Pereira et al.), which is the closest prior technique.

## Slide 9
LITERATURE SURVEY
Additional Related Work — Compiler Foundations & Systems
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
9
Work | Central contribution | Relevance to this project | Difference from our scope
Cytron et al. [9] ACM TOPLAS 1991 | Dominance-frontier algorithm for SSA and φ-function placement. | Provides the classical SSA construction foundation. | General SSA construction; our project uses SSA for range/integrality facts.
Lattner & Adve [10] CGO 2004 | LLVM IR and compiler pass framework for program analysis and transformation. | Supports the design principle of explicit IR and modular passes. | Industrial compiler infrastructure is outside v1 scope.
Ragan-Kelley et al. [11] PLDI 2013 | Halide separates algorithm description from scheduling for locality and parallelism. | Illustrates compiler-driven optimization under hardware constraints. | Targets image-processing pipelines and schedules, not per-value INT8 safety.
Chen et al. [12] OSDI 2018 | TVM provides an end-to-end optimizing compiler for deep-learning workloads. | Demonstrates an ML compiler stack with target-aware transformations. | Optimizes model graphs/operators at a larger scale than this teaching prototype.
Synthesis
Together, references [1]–[12] motivate edge-efficient numerical representations and establish the compiler/analysis foundations; this project combines them in a compact, inspectable pipeline.

## Slide 10
POSITIONING
Where This Project Fits
Existing industrial and research systems for quantization typically operate at a substantially larger model, compiler, or framework scale (e.g. whole deep-learning compilers or training frameworks).
This project instead focuses on a small, explainable compiler pipeline in which every quantization decision is directly justified by SSA structure, static range analysis, and integrality checking — making the underlying optimization principle easy to inspect and verify.
Existing Systems
Framework / Model / Compiler Scale
PROPOSED FOCUS
SSA + Range & Integrality Analysis + INT8 Safety Checking
Explainable compiler IR + static safety analysis + safe precision reduction
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
10
Notes: We are not claiming that no one has done quantization before — we're claiming a different, complementary focus: a compact compiler where the safety reasoning is fully explainable via SSA and range analysis, rather than folded into a large framework.

## Slide 11
METHODOLOGY
Compiler Pipeline Architecture
Source
Program
Lexer
Parser
AST
Semantic
Analysis
TAC
Basic Blocks
/ CFG
SSA
Range +
Integrality Analysis
INT8 Safety
Check
Quantization
Transform
Quantized
SSA IR
Simulator /
Backend
Diagnostics +
Evaluation
Shaded stages form the core static-analysis contribution of this project.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
11
Notes: The pipeline is a conventional front end — lexer, parser, AST, semantic analysis, TAC, CFG — followed by SSA construction and the project's core contribution: range and integrality analysis feeding an INT8 safety check, which gates the quantization transform before code generation and evaluation.

## Slide 12
REVIEW 2 · MODULE DESCRIPTIONS
Module Description I — Front End & Intermediate Representation
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
12
1. Lexer
Recognizes keywords, identifiers, literals and operators from source characters. It emits tokens with line/column positions.
Input: source text → Output: positioned tokens
2. Parser & AST
Checks the supported grammar and builds a structured Abstract Syntax Tree. Source locations remain attached to AST nodes.
Input: tokens → Output: AST
3. Semantic Analysis
Checks declarations and supported type/operand consistency before code generation. Invalid programs are reported rather than lowered.
Input: AST → Output: validated AST / diagnostics
4. TAC Generation
Lowers expressions and control flow into Three Address Code with temporaries, labels and conditional/unconditional branches.
Input: validated AST → Output: TAC
5. Basic Blocks & CFG
Partitions TAC into basic blocks and connects them with control-flow edges, including branches and loop back-edges.
Input: TAC → Output: CFG
6. SSA Construction
Versions variable definitions and inserts φ-nodes at control-flow joins/loop headers so every SSA value has one definition.
Input: CFG → Output: SSA IR
These stages establish the program structure and control-flow facts consumed by the analysis passes.

## Slide 13
REVIEW 2 · MODULE DESCRIPTIONS
Module Description II — Analysis, Transformation & Evaluation
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
13
7. Range & Integrality Analysis
Propagates interval bounds and whether values are guaranteed integral through supported SSA operations and φ-node merges. Loop widening is conservative and may yield UNKNOWN.
Input: SSA → Output: range + integrality facts
8. INT8 Safety Analysis
Checks whether the inferred interval lies within [−128,127], integrality is proven, and the operation is supported. If proof fails, it rejects quantization.
Input: analysis facts → Output: SAFE / REJECT + reason
9. Selective Quantization
Rewrites only operations certified safe by the preceding pass. Unsupported or unproven operations remain in their original representation.
Input: SSA + safety decisions → Output: quantized SSA/IR
10. Lightweight Simulator / Backend
Walks the original and transformed IR for functional comparison within the defined language. It is not an LLVM or hardware backend.
Input: original / quantized IR → Output: execution result
11. Diagnostics & Evaluation
Reports source line/column, inferred range, integrality, decision and rejection reason; tests correctness on supported programs. Hardware speed/energy are not measured.
Input: analysis + execution → Output: diagnostics / test evidence
Analysis decides; the transformation pass rewrites; the simulator checks functional behaviour. These are separate responsibilities.

## Slide 14
COURSE ALIGNMENT
Mapping to BCSE307L Concepts
The pipeline directly exercises core compiler-design concepts from the course syllabus:
BCSE307L Topic | Project Component
Intermediate Code Generation | Three Address Code (TAC)
Control Flow / Backpatching | Control Flow Graph (CFG) construction
Data-Flow Analysis | Static range & integrality analysis
Basic Blocks | CFG partitioning for analysis
Machine-Independent Optimization | Quantization transformation pass
Static Single Assignment (SSA) | SSA intermediate representation
Code Generation | Backend / lightweight simulator
Only concepts that genuinely contribute to the design are shown.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
14
Notes: Rather than force every syllabus topic in, we only show the concepts that genuinely map to a real component: intermediate code generation, CFG/backpatching, data-flow analysis, basic blocks, machine-independent optimization, SSA, and code generation.

## Slide 15
TECHNICAL MECHANISM
SSA Construction & Range Propagation
Source
x = 10
if (c)
x = 20
y = x + 5
SSA Form
x1 = 10
x2 = 20
x3 = φ(x1, x2)
y1 = x3 + 5
Inferred Ranges
Variable | Inferred Range
x1 | [10, 10]
x2 | [20, 20]
x3 | [10, 20]
y1 | [15, 25]
Range + Integrality
Quantization Decision
Range analysis propagates interval bounds through SSA operations; φ-nodes conservatively merge the ranges of incoming branches (union of bounds), so a value's range after a branch always covers every path that reaches it.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
15
Notes: A tiny example: x is assigned 10, conditionally reassigned to 20, and SSA introduces a phi node x3 merging both. Range analysis gives x3 the interval [10,20], and propagating through addition gives y1 the interval [15,25]. This range, plus integrality, feeds the quantization decision.

## Slide 16
DECISION LOGIC
Safe vs. Unsafe Quantization
CASE A — SAFE
x ∈ [10, 20], integral = true
10 ≥ −128 ✓
20 ≤ 127 ✓
→ SAFE: FP32 → INT8
CASE B — UNSAFE (Overflow)
x ∈ [120, 200], integral = true
200 > 127 ✗ (out of INT8 range)
→ REJECT: retain FP32
Edge Case —
Integrality Matters
x = 1.5 → range fits numerically, BUT integral = false → ✗ REJECT
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
16
Notes: Two symmetric cases show the decision rule directly: a range fully inside [-128,127] is quantized; a range that overflows is rejected. The bottom case is the key insight the project adds — x = 1.5 fits numerically but is not integral, so it must still be rejected.

## Slide 17
CONTROL FLOW
Handling Loops Safely
Example
i = 0
while (i < 100)
i = i + 1
Loop ranges must be computed via fixed-point iteration; naive propagation may not terminate.
A bounded / widening strategy guarantees the analysis converges to a conservative range in finite time.
CFG Construction
SSA φ-node at Loop Header
Range Propagation
Fixed-Point Convergence
Safe Termination
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
17
Notes: For a loop like this counter, SSA introduces a phi node at the loop header merging the initial and back-edge values. Range propagation must run to a fixed point; the analysis uses a bounded/widening strategy so it always converges and terminates, never looping forever trying to refine the range.

## Slide 18
DEMONSTRATION
Sample Compiler Diagnostics
Source
SSA Analysis
Range Report
Quantization
Decision
Quantized IR
Variable: z
Source: line 18, column 9
Range: [30, 60]
Integral: YES
INT8 Safety: PASS
Transformation: FP32 → INT8
Variable: x
Source: line 14, column 7
Range: [120, 200]
Integral: YES
INT8 Safety: FAIL
Reason: possible overflow
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
14
Notes: The compiler emits a diagnostic per variable: source location, inferred range, integrality, and the safety verdict. On the left, z is safely quantized. On the right, x is rejected with a clear, source-traceable reason — possible overflow at line 14, column 7.

## Slide 19
LIVE DEMONSTRATION · ORIGINAL TERMINAL CAPTURE
Demo A — Safe Arithmetic Is Accepted
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
19
OBSERVED IN CAPTURE
•
Command in the capture: examples/safe_arithmetic.qc with range, quantized IR and diagnostics output.
•
z.1 is inferred as [30,30] and is integral; the safety analysis accepts it.
•
The emitted IR rewrites x.1, y.1 and z.1 to int8; 3 analysed, 3 safe, 3 rewritten.
•
The supplied capture does not display a simulator run; simulator comparison is recorded separately in the verification summary.

## Slide 20
LIVE DEMONSTRATION · ORIGINAL TERMINAL CAPTURE
Demo B — Overflow Is Rejected
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
20
OBSERVED IN CAPTURE
•
Source example computes 100 + 30.
•
The result z.1 has inferred range [130,130], outside the INT8 upper bound 127.
•
The safety pass rejects z.1 for possible overflow; the unsafe result remains unquantized.
•
The safe operands x.1 and y.1 can still be rewritten independently.

## Slide 21
LIVE DEMONSTRATION · ORIGINAL TERMINAL CAPTURE
Demo C — If/Else SSA φ-Node and Range Merge
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
21
OBSERVED IN CAPTURE
•
The capture shows SSA and the φ-node for the if/else join.
•
The merged value max.4 has the inferred range [10,20] and is integral.
•
The unsupported relational comparison is left unquantized, consistent with the documented limits.
•
The report records matching original/quantized simulator output [20] = [20]; this capture shows analysis/IR, not that simulator run.

## Slide 22
REVIEW 2 · IMPLEMENTATION STATUS
From Proposed Architecture to Implemented Compiler Core
Source
Program
✓
Lexer
✓
Parser
✓
AST
✓
Semantic
Analysis
✓
TAC
✓
Basic Blocks
/ CFG
✓
SSA
✓
Range +
Integrality Analysis
✓
INT8 Safety
Analysis
✓
Selective
Quantization
✓
Quantized
SSA IR
✓
Lightweight
Simulator / Backend
✓
Diagnostics /
Evaluation
✓
✓ Implemented for the current teaching-scale scope. This is the 60% Review 2 milestone; remaining work focuses on coverage, backend maturity, and empirical evaluation.
REVIEW 1
Proposed architecture
Pipeline, IR choices and safety rules defined on paper.
REVIEW 2
Working compiler core
All stages run end-to-end for the current scope.
VERIFIED
20 / 20 tests passed
Plus 5 representative example programs, end-to-end.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
22
Notes: Since the first review, the project has moved from a proposed architecture to an implemented compiler core. Every stage of the pipeline from Review 1 now exists in code: lexer, parser and AST, semantic analysis, TAC, basic blocks and CFG, SSA, range and integrality analysis, INT8 safety analysis, selective quantization, quantized SSA IR, a lightweight simulator, and diagnostics. The pipeline runs end-to-end for the current scope and is backed by 20 passing automated tests and five representative example programs. This is a teaching-scale prototype, not a production compiler — the following slides show the evidence and the current limits.

## Slide 23
REVIEW 2 · COMPONENTS
Implemented Compiler Components
Component
Status
Evidence
Lexer
✓ Implemented
src/lexer/, lexer tests
Parser
✓ Implemented
src/parser/, parser tests
AST
✓ Implemented
src/ast/, AST tests
Semantic Analysis
✓ Implemented
src/semantic/, semantic tests
TAC Generation
✓ Implemented
src/ir/, TAC tests
CFG / Basic Blocks
✓ Implemented
src/cfg/, CFG tests
SSA Construction
✓ Implemented
src/ssa/, phi-node test and control-flow examples
Range Analysis
✓ Implemented
src/analysis/, interval propagation tests
Component
Status
Evidence
Integrality Analysis
✓ Implemented
Analysis tests and non-integral example
Loop Widening
✓ Implemented — Conservative
Loop analysis test and while-loop example
INT8 Safety Analysis
✓ Implemented
Quantization tests and rejection examples
Quantization Transformation
✓ Implemented
Quantization tests and safe arithmetic example
Backend / Simulator
✓ Implemented
Simulator and integration tests
Diagnostics
✓ Implemented
Diagnostic outputs with source locations
End-to-End Pipeline
✓ Implemented for Current Scope
Integration tests and example programs
Status and evidence as recorded in the Review 2 Report. Qualified entries are stated exactly as scoped: loop widening is conservative, and the end-to-end pipeline is complete for the current scope.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
23
Notes: This table is the implementation checklist from the Review 2 report, with the evidence for each component — the source module and the tests that exercise it. Thirteen components are fully implemented. Two are deliberately qualified: loop widening is implemented conservatively, and the end-to-end pipeline is implemented for the current scope of the language. The point is traceability: each claimed stage maps to code and to a test, rather than to a plan.

## Slide 24
REVIEW 2 · VERIFICATION
Test & Verification Results
20 / 20
AUTOMATED TESTS PASSED
Compiler test suite — 0 failures
Test run (verbatim)
python -m unittest discover -s tests -v
Ran 20 tests in 0.018s
OK
Representative programs examples/*.qc → analysis → quantized IR → simulator
✓
Safe arithmetic
examples/safe_arithmetic.qc
PASS
✓
Overflow rejection
examples/overflow_rejection.qc
PASS
✓
Non-integral rejection
examples/non_integral_rejection.qc
PASS
✓
If/else + SSA phi
examples/if_else_phi.qc
PASS
✓
While-loop + widening
examples/while_loop.qc
PASS
✓
Original vs quantized — if/else
simulator
[20] = [20]
✓
Original vs quantized — loop
simulator
[15] = [15]
Simulator rows compare execution of the original and the quantized SSA IR. In every tested case, unsafe or unproven values remain unquantized.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
24
Notes: This is the verification evidence. The full automated suite — 20 tests — passes, run with python -m unittest discover in about 18 milliseconds. On top of the unit tests, five representative programs go through the whole pipeline: a safe case, two rejection cases for overflow and non-integrality, an if/else that exercises SSA phi nodes, and a while loop that exercises widening. For the two control-flow programs the simulator runs both the original and the quantized IR and produces identical output: 20 and 15. What this shows is correctness on the tested programs — not a guarantee for every possible program.

## Slide 25
REVIEW 2 · VERIFICATION EVIDENCE
Authentic Test Suite Run
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
25
The supplied terminal capture shows the unittest discovery command completing with “Ran 20 tests” and “OK”. Test duration is run-specific.

## Slide 26
REVIEW 2 · COMPILER OUTPUT
Representative Output Summary — Accepted vs. Rejected
SAFE ARITHMETIC — ANALYSIS examples/safe_arithmetic.qc
Source:
int x = 10; int y = 20; int z = x + y; print z;
Analysis result:
x.1 -> [10,10] -> SAFE
y.1 -> [20,20] -> SAFE
z.1 -> [30,30] -> SAFE
3 analysed, 3 safe, 3 rewritten, 0 rejected.
SAFE ARITHMETIC — QUANTIZED IR selective quantization output
Quantized IR:
x.1 : int8 = 10
y.1 : int8 = 20
z.1 : int8 = x.1 + y.1
OVERFLOW REJECTION examples/overflow_rejection.qc
Source:
int x = 100; int y = 30; int z = x + y; print z;
Analysis result:
x.1 -> [100,100] -> SAFE
y.1 -> [30,30] -> SAFE
z.1 -> [130,130] -> REJECTED
Reason: possible overflow (130 > 127)
3 analysed; 2 rewritten, 1 rejected.
NON-INTEGRAL REJECTION examples/non_integral_rejection.qc
Source:
float x = 10.0; float y = 3.5; float z = x + y; print z;
Analysis result:
x.1 -> [10,10] -> integral -> SAFE
y.1 -> [3.5,3.5] -> non-integral -> REJECTED
z.1 -> [13.5,13.5] -> non-integral -> REJECTED
3 analysed, 1 safe, 1 rewritten, 2 rejected.
Typeset summary from the report; genuine terminal captures are shown on demo slides 19–21. Rejection is per value: safe operands may still be quantized when a dependent result is rejected.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
26
Notes: These are actual outputs from the compiler, not mock-ups. On the left, the safe program: every SSA value has a known integral range inside INT8, so all three are rewritten and the quantized IR types them as int8. On the right, the same addition with 100 plus 30: z.1 is 130, which exceeds 127, so it is rejected with an explicit reason. Below it, 3.5 is in range numerically but is not integral, so it and the sum that depends on it are rejected. Rejection is selective — the safe operands in each program are still quantized.

## Slide 27
REVIEW 2 · CONTROL FLOW
Control-Flow Verification: φ-Nodes & Loops
IF / ELSE + SSA φ examples/if_else_phi.qc
B3 · max.3
B4 · max.2
max.4 = phi(B3: max.3, B4: max.2)
max.4 -> [10,20] integral = YES
t1 = x.1 > y.1 → rejected, left unquantized: relational ‘>’ is not supported by the quantization pass
ORIGINAL SSA EXECUTION
[20]
=
QUANTIZED SSA EXECUTION
[20]
WHILE LOOP + WIDENING examples/while_loop.qc
Loop (back edge → φ at header)
Range Propagation
Widening
Conservative Convergence
SAFE / UNKNOWN Decision
Termination by design
Iteration at the loop header is bounded by a widening threshold.
If the range does not stabilise in time, the value becomes UNKNOWN.
UNKNOWN values are never quantized.
ORIGINAL SSA EXECUTION
[15]
=
QUANTIZED SSA EXECUTION
[15]
Report summary of simulator comparisons; the genuine terminal capture on demo slide 21 shows the SSA/phi and range output. Reported original/quantized outputs match for the tested control-flow programs.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
27
Notes: Straight-line code is the easy case, so this slide shows control flow. In the if/else program, SSA inserts a phi node at the join, max.4 equals phi of max.3 from B3 and max.2 from B4, and range analysis merges the branches to [10, 20], integral. The comparison temporary using the greater-than operator is not supported by the quantization pass, so it is left unquantized. In the while loop, the analysis uses conservative widening: if a range does not stabilise within the threshold it becomes UNKNOWN and is not quantized. In both programs the simulator gives the same output before and after quantization: 20 and 15. The trade-off is coverage: widening may give up on some loop values that are actually safe.

## Slide 28
REVIEW 2 · SCOPE
Current Limitations & Remaining Work
1
Loop widening is conservative
Can produce UNKNOWN for loop-carried values when the range does not stabilise within the configured widening threshold. Such values stay unquantized — safe, but less coverage.
2
Unsupported operations are not quantized
Operations outside the supported set — e.g. the relational comparison ‘>’ — are left untouched. Retained in their original form.
3
Lightweight backend
The backend is an IR-walking simulator, not LLVM and not a real hardware backend. Used to compare original vs. quantized execution.
4
No empirical performance measurements yet
Runtime, latency, energy and hardware-power have not been measured. No speed-up or energy gain is claimed at this milestone.
60% MILESTONE — WHERE WE STAND
Working compiler core for the current scope
✓ Teaching-scale prototype, verified on representative programs
✓ 20/20 automated tests passed
✓ Safe integer-valued SSA operations lowered to int8
✓ Unsafe or unproven values remain unquantized
Limitations as stated in the Review 2 Report. None of them weakens the core rule: unsafe or unproven values remain unquantized.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
28
NEXT PHASE
Extend operation coverage • improve loop precision • develop a more realistic backend • measure runtime/energy
Notes: To keep this grounded, here is exactly what the prototype does not do yet. Loop widening is conservative and can return UNKNOWN; operations like the greater-than comparison are not quantized; the backend is a lightweight IR simulator rather than LLVM or real hardware; and we have not yet measured runtime, latency, energy or power, so we make no performance claims. Note that every limitation fails safe — when in doubt, the compiler leaves the value unquantized. At this 60 percent milestone we have a working compiler core for the current scope, verified on representative programs.

## Slide 29
OUTCOME
Project Outcome
Within the current supported scope, the compiler produces three concrete outcomes — each one backed by a compile-time proof rather than a runtime check.
1
Static Safety Check
Verifies at compile time that a value stays integral and remains within [−128, 127] across all execution paths.
2
Selective Quantization
Rewrites only certified-safe operations into INT8, leaving every uncertain operation untouched in FP32.
3
Traceable Output
Emits line-by-line diagnostics stating whether each variable was converted or rejected, and the specific reason.
4×
Reduction in memory per quantized value — 4 bytes (FP32) → 1 byte (INT8), with potential for efficient integer arithmetic on suitable hardware; only values proven safe within the supported model are transformed.
Memory reduction follows directly from the width change; runtime and energy gains remain to be measured.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
29
Notes: To close, the project delivers three outcomes. First, a static safety check that proves at compile time that a value stays integral and inside the INT8 range on every execution path. Second, selective quantization — only certified-safe operations are rewritten to INT8, and anything unproven stays FP32. Third, a traceable output: line-by-line diagnostics saying whether each variable was converted or rejected, and why. The memory outcome is a 4x reduction per quantized value, which follows directly from the 4-byte to 1-byte width change; runtime and energy gains we will measure rather than assume. Thank you.

## Slide 30
REFERENCES
References
[1] Z. Zhou, X. Chen, E. Li, L. Zeng, K. Luo, and J. Zhang, “Edge intelligence: Paving the last mile of artificial intelligence with edge computing,” Proc. IEEE, vol. 107, no. 8, pp. 1738–1762, Aug. 2019.
[2] J. Chen and X. Ran, “Deep learning with edge computing: A review,” Proc. IEEE, vol. 107, no. 8, pp. 1655–1674, Aug. 2019.
[3] B. Jacob, S. Kligys, B. Chen, M. Zhu, M. Tang, A. Howard, H. Adam, and D. Kalenichenko, “Quantization and training of neural networks for efficient integer-arithmetic-only inference,” in Proc. IEEE Conf. Computer Vision and Pattern Recognition (CVPR), 2018, pp. 2704–2713.
[4] R. Krishnamoorthi, “Quantizing deep convolutional networks for efficient inference: A whitepaper,” arXiv:1806.08342, 2018.
[5] P. Cousot and R. Cousot, “Static determination of dynamic properties of programs,” in Proc. 2nd Int. Symp. on Programming (ISOP), Paris, France: Dunod, 1976, pp. 106–130.
[6] P. Cousot and R. Cousot, “Abstract interpretation: A unified lattice model for static analysis of programs by construction or approximation of fixpoints,” in Proc. 4th ACM SIGACT-SIGPLAN Symp. on Principles of Programming Languages (POPL), 1977, pp. 238–252. PTO
References [7]–[12] —PTO.
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
30

## Slide 31
REFERENCES
References (Continued)
BCSE307L — Compiler Design | Range-Aware Edge AI Quantization Compiler
31
[7] F. Bourdoncle, “Efficient chaotic iteration strategies with widenings,” in Formal Methods in Programming and Their Applications, LNCS vol. 735. Berlin, Germany: Springer, 1993, pp. 128–141.
[8] B. Blanchet, P. Cousot, R. Cousot, J. Feret, L. Mauborgne, A. Miné, D. Monniaux, and X. Rival, “A static analyzer for large safety-critical software,” in Proc. ACM SIGPLAN Conf. on Programming Language Design and Implementation (PLDI), 2003, pp. 196–207.
[9] R. Cytron, J. Ferrante, B. K. Rosen, M. N. Wegman, and F. K. Zadeck, “Efficiently computing static single assignment form and the control dependence graph,” ACM Trans. Program. Lang. Syst., vol. 13, no. 4, pp. 451–490, Oct. 1991.
[10] C. Lattner and V. Adve, “LLVM: A compilation framework for lifelong program analysis and transformation,” in Proc. Int. Symp. on Code Generation and Optimization (CGO), 2004, pp. 75–86.
[11] J. Ragan-Kelley, C. Barnes, A. Adams, S. Paris, F. Durand, and S. Amarasinghe, “Halide: A language and compiler for optimizing parallelism, locality, and recomputation in image processing pipelines,” in Proc. ACM SIGPLAN Conf. on Programming Language Design and Implementation (PLDI), 2013, pp. 519–530.
[12] T. Chen, T. Moreau, Z. Jiang, L. Zheng, E. Yan, M. Cowan, H. Shen, L. Wang, Y. Hu, L. Ceze, C. Guestrin, and A. Krishnamurthy, “TVM: An automated end-to-end optimizing compiler for deep learning,” in Proc. 13th USENIX Symp. on Operating Systems Design and Implementation (OSDI), 2018, pp. 578–594.